## Slide 1
PREDICTIVE MAINTENANCE PROJECT
Predicting Remaining Unit Life of Turbojet Engine
Regression-based estimation of engine degradation using the NASA C-MAPSS FD001 sensor dataset.
Prepared by
BAIBHAB CHOWDHURY
Roll: 0738
Reg. No. - 012-1111-1008-21
Theme: Remaining Useful Life (RUL) prediction for turbofan engines
01 / 08
Notes: Opening slide with student credentials, exact topic wording from the user, and the project framing.
[Sources]
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.

## Slide 2
02 / 08
PROJECT ABSTRACT
Why this project matters
Predictive maintenance aims to estimate failure early enough to plan maintenance before breakdown.
This project predicts the Remaining Useful Life (RUL) of turbofan
engines from multivariate time-series sensor readings in the NASA
C-MAPSS FD001 dataset. The workflow creates cycle-wise RUL targets,
removes near-constant columns, engineers rolling statistical
features, scales the predictors, and then compares linear, lasso, and
ridge regression models. A reliable RUL estimate helps schedule
inspection or component replacement before complete failure, which
supports safer operation and reduces unexpected downtime.
Objective
Estimate how many operating cycles
remain before an engine needs
maintenance using cycle, setting, and
sensor data.
Outcome
The model converts sensor history
into an early maintenance forecast,
reducing unexpected failure and
reactive repair.
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Abstract slide summarizing the goal, workflow, and practical relevance.
[Sources]
- NASA C-MAPSS FD001 turbofan engine degradation dataset used in the project repository.
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.

## Slide 3
03 / 08
CHOSEN DATASET
NASA C-MAPSS FD001
The project uses one operating-condition subset of the simulated turbofan degradation benchmark.
What it is
FD001 is a run-to-failure turbofan engine
dataset. Each row records one engine cycle
with engine id, cycle index, 3 operational
settings, and 21 sensor measurements. The
training split contains 100 engines observed
until failure.
20,631
rows in train_FD001.txt
26
raw columns before RUL
100
unique engines
46
columns after engineering
27
columns after
adding RUL target
17
columns after
column filtering
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Dataset slide with the exact row and column counts pulled from the repository data files.
[Sources]
- NASA C-MAPSS FD001 turbofan engine degradation dataset used in the project repository.
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.

## Slide 4
04 / 08
COLUMN REMOVAL
Near-zero-variance features were removed before modeling
Flat columns contribute little information because they barely change across engines or cycles.
How it was done
The notebook computed variance for
every operational setting and
sensor on train_FD001_with_RUL.csv.
Any field satisfying
round(variance, 5) < 1e-10 was
treated as effectively constant and
then dropped from the cleaned
dataset.
Removed settings
• setting_1
• setting_2
• setting_3
Removed sensors
• s_1, s_5, s_6, s_10
• s_16, s_18, s_19
Result: 10 low-information columns were removed, reducing the dataset from 27 columns to 17 columns and retaining 14 active sensors for modeling.
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Column-filtering slide showing what was removed, why the columns were unhelpful, and the variance-based rule used in the notebook.
[Sources]
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.

## Slide 5
05 / 08
FEATURE ENGINEERING
Why and how the features were constructed
The cleaned cycle-wise sensor table was transformed into features that better describe degradation dynamics.
Rolling Mean
For each active sensor, a
5-cycle rolling mean was
computed within each
engine. This smooths
noise and highlights
local degradation trend.
Rolling Std
A 5-cycle rolling
standard deviation was
also created. It captures
short-term instability
and fluctuation
intensity.
RUL Clipping
The target was clipped at
125 cycles. This
piecewise target reduces
the influence of very
large early-life RUL
values.
Scaling
Min-Max scaling
put all predictors
on a comparable
range before
regression
training.
Engineering summary: 14 active sensors produced 28 rolling statistics (14 means + 14 standard deviations). The final modeling file contains 46 columns including identifiers and targets.
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Feature-engineering slide explaining the rolling statistics, clipped target, scaling step, and why each step is useful for this problem.
[Sources]
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.

## Slide 6
06 / 08
MODELING WORKFLOW
How the prepared data was turned into a regression task
The pipeline preserves engine chronology and avoids leakage between training and validation engines.
Raw FD001
Engine cycle data
with settings and
sensors.
Add RUL
RUL = max cycle per
engine minus
current cycle.
Clean Columns
Drop near-flat
settings and
sensors.
Engineer Features
Rolling mean,
rolling std,
clipping, and
scaling.
Fit Models
Train the three
regression models.
Train / validation split
Engines 1-80 were used for training and engines
81-100 for validation. Splitting by engine avoids
leaking later cycles of the same engine across both
sets.
Feature-target definition
X contains engineered predictors only. unit_nr,
time_cycles, RUL, and RUL_clipped were excluded from X,
while y was defined as RUL_clipped.
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Workflow slide covering target creation, feature preparation, and the engine-level train/validation split.
[Sources]
- Project notebooks and processed CSV files in this repository: data/raw, data/processed, notebooks/01-04.
- Validation metrics recomputed from train_FD001_engineered.csv using Linear Regression, Lasso Regression, and Ridge Regression.

## Slide 7
07 / 08
REGRESSION MODELS COMPARED
Only three models were evaluated for the final comparison
All three models share the same feature set and validation split so their metrics remain directly comparable.
Linear Regression
Acts as the baseline model. It
estimates one weight per feature
and shows how much predictive
power is already present in the
engineered linear relationships.
Lasso Regression
Adds L1 regularization. It can
shrink weak coefficients to zero,
which is useful when many
engineered features may be
redundant or only weakly
informative.
Ridge Regression
Adds L2 regularization. It keeps
all features but stabilizes the
coefficients when correlated
sensor trends exist in the
engineered dataset.
Evaluation metrics: RMSE measures large errors strongly, MAE measures average absolute error directly, and R² measures how much target variance is explained by the model.
Source: NASA C-MAPSS FD001 and project notebooks
Notes: Model-comparison setup slide limited to linear, lasso, and ridge regression with the reasons each model is relevant.
[Sources]
- Validation metrics recomputed from train_FD001_engineered.csv using Linear Regression, Lasso Regression, and Ridge Regression.

## Slide 8
08 / 08
FINAL RESULTS
Lasso Regression gave the best overall validation result
The three models performed very similarly, but lasso achieved the smallest RMSE and tied for the lowest MAE.
Model
RMSE
MAE
R²
Linear Regression
20.8815
16.9817
0.7441
Lasso Regression
20.8805
16.9817
0.7441
Ridge Regression
20.8814
16.9823
0.7441
Best model
Lasso Regression is the best model in
this comparison because it achieved
the lowest RMSE (20.8805 cycles) while
matching the lowest MAE. Its R² is
also on par with the other two models.
Interpretation
Scores are nearly identical, so
feature engineering contributes more
than regularization to final accuracy.
Source: metrics recomputed from train_FD001_engineered.csv with the same engine split
Notes: Closing slide with the exact validation metrics and the final model selection statement.
[Sources]
- Validation metrics recomputed from train_FD001_engineered.csv using Linear Regression, Lasso Regression, and Ridge Regression.